## Slide 1: SDN: Emulation, Implementation and Load Balancing

## Slide 2: Traditional Network

## Slide 3: What’s Networking
A network is a group of two or more computer systems linked together

## Slide 4: Network components

## Slide 5: Network Models

## Slide 6: Network Types
LAN
MAN
WAN
VPN

## Slide 7: Network Architecture
Device Planes :

## Slide 8: Network Architecture
In the traditional network architecture, control plane and data plane are integrated and any changes to the system are dependent upon physical network devices, the protocols and software they support. Limited changes can be performed to the overall system as the network devices bottleneck logical network traffic flows.

## Slide 9: Network Infrastructure
It consists of core layer switches which connect to distribution layer switches (sometimes called aggregation switches), which in turn connect to access layer switches. Access layer switches are frequently located at the top of a rack, so, these are also known as top-of-rack (TOR) switches. Most network infrastructure is still laid out this way today.

## Slide 10: Software Defined Network

## Slide 11: SDN Technology
Software-Defined Networking (SDN) technology is an approach to cloud computing that facilitates network management and enables programmatically efficient network configuration in order to improve network performance and monitoring.

## Slide 12: Why We Need SDN?
Virtualization
Orchestration
Programmable
Dynamic Scaling.
Automation
Visibility
Performance
Multi-tenancy
Service Integration

## Slide 13: SDN Architecture
SDN broadly consists of three layers:
  Application layer
  Control layer
  Infrastructure layer

## Slide 14: Control Layer
Northbound interface: is meant for communication with upper, Application layer and would be in general realized through REST APIs of SDN controllers.
Southbound interface: is meant for communication with lower, Infrastructure layer of network elements and would be in general realized through southbound protocols OpenFlow, Netconf, Ovsdb, etc.
The east-west interfaces: which are not yet standardized, allow communication between the multiple controllers. They use a system of notification and messaging or a distributed routing protocol like BGP and OSPF.

## Slide 15
Advantage
Directly programmable
Agile
Centrally controlled:
Open standards-based
Network management Simplicity
Fast service deployment
Automated configuration
Saving cost, effort and time
CAPEX reduction
Disadvantage
Software Defined Network
It requires change in entire network infrastructure to implement SDN protocol and SDN controller.
Staff need to be trained.
Single point of failure.
Security is a big challenge in SDN.
New management tools need to be procured and everyone should be trained to use it.

## Slide 16: Traditional Network VS. SDN
There are three most important differences between traditional networking and SDN.
First, the SDN controller has a northbound interface that communicates with applications via application programming interfaces (APIs).
Second, SDN is a software-based network, which allows users to control virtual-level resource allocation through the control plane and to determine network paths and proactively configure network services.
Third, SDN has more ability to communicate with devices throughout the network than traditional networking.

## Slide 17: Traditional Network VS. SDN Cont.
Traditional Network
SDN
Traditional Network - Configuration complexity increases the need for synchronization which limits performance of devices.
SDN network, modular control and central view of network components.

## Slide 18
Component | Cost
Switch 2960 | 4000$*4=16000 USD
Switch 3560 | 9000$* 2 = 18000 USD
Router 2911 | 9000$
RAC and Power Distribution and cables | 2000$
PC For each employee | 500 USD * 50 = 25000 USD
Component | Cost
SDN controller | 4000$
Open virtual switch | 2000$*6=12000$
PC For each employee | 500 USD * 50 = 25000 USD
Traditional Network VS. SDN Cont.
Total cost = AROUND 41,000 USD
Total cost = AROUND 80,000 USD

## Slide 19: OPENFLOW Protocol

## Slide 20: OPENFLOW Protocol
OpenFlow is an open standard protocol specifically designed for the SDN networks that allows the communication between the control and data planes.

## Slide 21: OpenFlow Architecture
OpenFlow switches that compose the data plane.
The control plane consists of one or more OpenFlow controllers.
A secure control channel connects the switches with the control plane.

## Slide 22: Open flow switch
The OpenFlow-enabled switch is the basic forwarding device that forwards the packets according to its flow table which is similar to traditional forwarding tables but not managed and maintained by the switch.

## Slide 23: OpenFlow Switch Ports
Physical ports
Logical ports
Reserved ports:-
  All
  Table
  Controller
  In port
  Any
  NORMAL
OpenFlow ports are the network interfaces for passing packets between OpenFlow processing and the rest of the network.

## Slide 24: OpenFlow Table Entry

## Slide 25: Packet Process Mechanism for OpenFlow Switch

## Slide 26: OpenFlow Switch Actions
Forward
ALL
CONTROLLER
Drop

## Slide 27: Pipeline Processing
OpenFlow-compliant switches come in two types:
OpenFlow only
OpenFlow hybrid

## Slide 28: Flow types
Flows populated from the OpenFlow controller can be classified into types:
Reactive
Proactive

## Slide 29: OpenFlow Communication Messages
Controller-to-switch
Modify-State
Read-State
Features
Send-Packet
Asynchronous Messages
Packet-in
Port-status
Error
Flow-Removed
Hello
Echo
Symmetric

## Slide 30: OpenFlow Communication Messages Cont.
Message establishment between a switch and a controller

## Slide 31: OpenFlow Communication Messages Cont.
Messages exchanged between two hosts.

## Slide 32: Mininet

## Slide 33: What’s Mininet?
A network emulator which creates realistic virtual network.
It runs a collection of end-hosts, switches, routers, and links on a single Linux kernel.
Provides both Command Line Interface (CLI) and Application Programming Interface (API)
  CLI: interactive commanding
  API: automation
The code used in Mininet can be used with no or minimal changes on real SDN OpenFlow networks.
A design that works in Mininet can usually move directly to hardware switches.

## Slide 34: Why Mininet?

## Slide 35: Mininet command line Interface usage
Mininet default topologies
Mininet Custom Topologies
$ sudo mn
$sudo mn --topo=single,3 --mac --controller=remote switch=ovsk,Protocols=OpenFlow1

## Slide 36: MiniEdit
Create your network topology.
Save: for MiniEdit data file.
File >> save
Export: for Mininet script file.
File >> export
To run the exported script:
% sudo SAVE_FILE_NAME.py
Run Mininet from MiniEdit.
Run >> Run

## Slide 37: SDN Controllers

## Slide 38: The General description of a SDN Controller
An SDN controller is an application in a software-defined networking (SDN) architecture that manages flow control for improved network management and application performance.
The controller is the core of a software-defined network. It resides between network devices at one end of the network and applications at the other end. Any communication between applications and network devices must go through the controller.

## Slide 39: List of SDN Controllers
Open-Source Controllers
Commercial Controllers
Active Resource Controller
Calsoft Labs Virtual WLAN Controller
Cisco Application Policy Infrastructure Controller (APIC)
Cisco Application Policy Infrastructure Controller (APIC) Enterprise Module
CPLANE NETWORKS Controller
Embedded Systems Software Development in Networking
Extreme Networks Slalom
HP Virtual Application Networks (VAN) SDN Controller
IBM Programmable Network Controller
Inocybe Infrastructure Controller
Italtel Session Border Controller

## Slide 40: HPE VAN
provides a unified control point in an OpenFlow-enabled network, simplifying management, provisioning, and orchestration and enabling delivery of a new generation of application-based network services.
List of controller embedded applications:
• OpenFlow Link Discovery
• OpenFlow Node Discovery
• Path Diagnostics
• Topology Manager
• Topology Viewer

## Slide 41: Running HPE VAN
Step 1 : Import virtual Machine
Step 2 : Assign Static ip

## Slide 42
Step 3: Create Simple topology and Define Controller Machine
Step 4: Connect to HPE VAN GUI
$ sudo mn -- controller=remote,ip=192.168.236.138
Running HPE VAN

## Slide 43: Running HPE VAN
Step 5: Sudo mn Output
Step 6: Flow Table

## Slide 44: RYU
Ryu Controller is an open, software-defined networking (SDN) Controller designed to increase the flexibility of the network by making it easy to manage and adapt how traffic is handled.

## Slide 45: RYU Architecture

## Slide 46: Ryu Applications
Simple Switch
STP
Simple Monitor
Rest Router

## Slide 47: Simple L2 Switch Application
Topology
Results

## Slide 48: STP Application
Spanning tree is a function that suppresses occurrence of broadcast streams in a network having a loop structure. Also, applying the original function that is preventing the loop, it is used as a means to secure network redundancy to automatically switch the path in case of a network failure.

## Slide 49: STP Overview
Selecting the root bridge:
Root port
Designated ports
Non designated ports

## Slide 50: STP Application
Topology Using MiniEdit
Topology Commands

## Slide 51: STP Application
BPDU Exchange
Packets Flow

## Slide 52: STP Application
As a result of tcpdump
output, you can confirm
that ARP is not looped

## Slide 53: STP Application
Try Link S1 – S3 Down
Detect Failure , Recalculate

## Slide 54: Pox
POX is an open source development platform for Python-based software-deﬁned networking (SDN) control applications, such as OpenFlow SDN controllers.
It is a popular tool for teaching about and researching software deﬁned networks and network applications programming
POX Features
Pythonic OpenFlow interface.
Reusable sample components for path selection, topology discovery, etc.
Speciﬁcally targets Linux, Mac OS, and Windows.

## Slide 55: POX Components
forwarding.hub: The hub example just installs wildcarded flood rules on every switch
forwarding.l2_learning: This component makes OpenFlow switches act as a type of L2 learning switch
forwarding.l3_learning:
./pox.py forwarding.l3_learning --fakeways=10.0.0.1,192.168.0.1

## Slide 56: Forwarding.hub
Running Controller
Checking traffic

## Slide 57: forwarding.l2_learning
Problem
Running Controller

## Slide 58: forwarding. l2_learning
This component makes OpenFlow switches act as a type of L2 learning switch

## Slide 59: Making Custom Topology

## Slide 60: Load Balancing, How The System works ?

## Slide 61: Load balancing algorithms
Random-based: The controller selects one server randomly from the available servers for each request.
Round-robin: This technique distributes the requests among the servers in a sequential manner.
Connections-based: This algorithm chooses the server based on minimum active connections.

## Slide 62
Step 1
Step 2
Load Balancing Algorithms

## Slide 63: Load Balancing Algorithms
Step 3
Step 4

## Slide 64: Round Robin
Weighted round robin:
It can be used effectively for a cluster of unidentical servers as each server is assigned a weight based on its structure and efficiency.
Dynamic round robin:
It forwards the requests to the associated server based on a real-time calculation of server weights.

## Slide 65: Other Algorithms
Bandwidth-based (BWBLB)
Server CPU-based (CBLB)
Server CPU-Memory-based (CMBLB)
The least response time
URL hash
Source IP hashThe
The least bandwidth and the
least packets method
The custom load method

## Slide 66: Round Robin Applied
Process
Result

## Slide 67: Round Robin and Random

## Slide 68: Tools

## Slide 69: Openload
Definition
OpenWebLoad is a tool for load testing web applications. It aims to be easy to use and providing near real-time performance measurements of the application under test.
Options
-t
-h
-l
openload [options] url [clients]

## Slide 70: Openload
Results:
Parameters:
MaTps
Tps
Total TPS is the average TPS for the whole run, i.e. (Total completed requests) / (Total elapsed time).
Avg. Response time
Max Response time
$ openload localhost 10

## Slide 71: SIEGE
Definition
Siege is a Hypertext Transfer Protocol (HTTP) and HTTPS load testing and web server benchmarking utility developed by Jeffrey Fulmer.
Options
C
c
t
d
b
H
$ siege -f /usr/local/etc/urls.txt

## Slide 72: SIEGE
Output By Domain
$ siege domain.name

## Slide 73: Httpref
Definition
Httpref is a tool for measuring web server performance. It provides a flexible facility for generating various HTTP workloads and for measuring server performance.
Steps
appropriate timeout values
Total Results
Connection Results
Request Results
Reply Results
Miscellaneous Results
httperf --server wailua --port 6800
httperf --server wailua--port 6800
--num-conns100 --rate10--timeout 1

## Slide 74: Httpref
Error
total
socket-timo
Connrefused
Connreset
Other
Output